## Slide 1: OCI Systems Engineer Eric Gorman
Plankton, Aerosol, Cloud, ocean Ecosystem (PACE)
OCI Overview
June 2, 2020

## Slide 2
hyperspectral scanning radiometer
340 – 890 nm, 5 nm resolution, 2.5 nm steps
plus, 940, 1038, 1250, 1378, 1615, 2130, and 2250 nm
1 – 2 day global coverage
ground pixel size of 1 km2 at nadir
± 20o fore/aft tilt to avoid Sun glint
twice monthly lunar calibration
daily on-board solar calibration
built at NASA Goddard Space Flight Center
Notes: OCI overview part 1 – general characteristics

## Slide 3
OCI Fundamentals Agenda
Telescope Slit
Rotating Telescope
Slit Grating UVNIR Spectrograph
Time Delay Integration
NIRSWIR Fiber Coupled Spectrograph
Tilt It!

## Slide 4
Telescope Slit Ground Image
The telescope images sixteen 1km science pixels onto a slit
16km cross track x 1km along track
The slit is imaged onto the detector of each spectrograph
16 Science Pixels, 1000m Each, 16km Total
Telescope Slit Image
*Approximate Scale

## Slide 5
Rotating Telescope
The rotating telescope moves the ground image across the slit in the cross track direction
~1200 science pixels for each telescope rotation
Telescope rotation rate of ~5.7Hz is set to avoid gaps between ground scans

## Slide 6: Rotating Telescope and Half Angle Mirror Fundamentals
RT
HAM
RT
HAM
RT
HAM
RT
RT
HAM
HAM
Slit
Rotating Telescope (RT)
  Off Axis Parabola Primary Mirror
  Continuous 360o Rotation ~5.7 Hz
  Sweeps across the full field of regard
Half Angle Mirror (HAM)
  Double Sided Flat Mirror
  Continuous 360o Rotation ~RT/2 Hz
  Reflects ground image from rotating primary mirror onto the stationary slit
Field of Regard +/- 55o
Scan Direction
(West to East)
Scene
Scene
Scene
Scene
Scene

## Slide 7
Spectrograph wavelengths are selected by a dichroic
885nm
600nm
605nm
340nm
VISNIR Slit-Grating Spectrograph
UVVIS Slit-Grating Spectrograph
UVNIR Slit Grating Spectrograph
Telescope Slit Image
A grating spectrally separates the slit/ground image
The same slit/ground image is focused onto each detector in 5nm steps with 5nm bandwidth

## Slide 8
Synchronization of the CCD readout with the rotating telescope enables time delay integration (TDI)
The CCD uses TDI to transfer the charge from pixel to pixel at the same rate of the rotating telescope. This occurs in analog charge space to avoid noise introduced by reading, amplifying, and digitizing the signal
TDI allows the detection system to view the same ground scene for an extended time and build up enough signal to meet SNR while eliminating image striping due to detector pixel gain offsets
16 Science Pixels-1000m Each, 16,000m Total
Time Delay Integration

## Slide 9
Time Delay Integration
The UVVIS & VISNIR spectrographs produce a continuous stream of data
109 spectral bands for each 1km science pixel
Ground scene moving across the slit
On-chip TDI across the detector

## Slide 10
OCI Optical System – Optical Module

## Slide 11
Read 1
Read 2
Read 3
Read 4
The slit is imaged onto a micro lens array
Light from the MLA image is fiber coupled to the NIRSWIR bandpass-photodiode focal planes
The FPA readout is synchronized with the rotating telescope
Digital TDI is shown to the right
Read 5
Read 6
Read 7
Read 8
Read 9
Example: TDI 8
Blue – 1st scene
Red – 2nd scene
Telescope Slit Image
NIRSWIR Fiber Coupled Spectrograph

## Slide 12
Tilt It!
OCI is mounted to a tilt mechanism system
Around the subsolar point, the nadir boresight is tilted +/- 20 degrees in the along track direction in less than a minute

## Slide 13: OCI Description (1/2)
Optical Module (OM)
Rotating Telescope Assembly
Half Angle Mirror
Slit Grating UVVIS Hyperspectral Spectrograph
Slit Grating VISNIR Hyperspectral Spectrograph
Solar Calibration Assembly (SCA)
Integrated carousel mechanism
  3 Calibration Targets
Integrated Baffle
SWIR Detection Assembly (SDA)
NIR-SWIR Fiber Coupled Multiband Filter Spectrograph
Electronics
Radiators & Earth Shield

## Slide 14: OCI Description (2/2)
UVVIS & VISNIR Focal Plane Assemblies
CCD with On-Chip TDI and Integrated ADC
Data Acquisition Unit
CCD Clock and Bias
SDA Power
Data Processing
Motor Control Electronics
Instrument Command & Data Unit
Processor
House Keeping
Thermal Control
Power Distribution
Radiator Earth Shield
UVVIS & VISNIR FPA Loop Heat Pipes

## Slide 15: OCI Engineering Hardware Development Status
Structure
ICDU
FSW
Not Started
In Process
Complete
Key
MCE
Harness
Electrical System
Red FPA
MOB
DAU
MOSB
MLA&Fiber
Optical Module
OCI CPT
CPT &
Pre-Launch Calibration Hardware
I&T Backend Infrastructure
FEDS
ITOS
SWITS
XINA
GATOR
GLAMR
Radiometers
Sources
OCI TVAC
SDA Integration & Test
SDA
Pre-Launch Calibration Pathfinder
Red FPA
Blue FPA
SSM

## Slide 16
Optical Module Testing

## Slide 17
VISNIR Focal Plane Alignment

## Slide 18
Electronics Integration

## Slide 19
OCI – Ready To Test

## Slide 20
Comprehensive Performance Testing – Ambient

## Slide 21
NASA/GSFC – GLAMR Tunable Laser

## Slide 22
Comprehensive Performance Testing – TVAC

## Slide 23
SWIR Detection Assembly – Ready For Integration

## Slide 24: OCI Engineering Hardware Test Results

## Slide 25: OCI Flight Hardware Development Status
Structure
ICDU
FSW
Not Started
In Process
Complete
Key
MCE
Harness
Electrical System
MOB
DAU
MOSB
MLA&Fiber
Optical Module
OCI CPT
CPT &
Pre-Launch Calibration Hardware
I&T Backend Infrastructure
FEDS
ITOS
SWITS
XINA
GATOR
GLAMR
Radiometers
Sources
Environmental Testing
Calibration
SDA
Integrate w/ Spacecraft
Red FPA
Blue FPA

## Slide 26: OCI Instrument Specs
Instrument Mass | 260 kg CBE , 305 kg NTE
Instrument Power | 280 W CBE , Orbital Average
Thermal System | Passive Cooling with Loop Heat Pipes
Mechanisms | Rotating Telescope Mechanism (~6Hz) Half Angle Mirror Mechanism (~3Hz) Solar Calibration Mechanism (5000 Cycle)
Deployments | Rotating Telescope Launch Lock
Ground Sample Distance | 1050m at Nadir
Aperture | 93mm
iFOV | 0.08o Along Track x 1.42o Cross Track
UVNIR System EFL | 0.134m
UVNIR System f/no | 1.49
Total Field of Regard | +/- 55o
Dynamic Range | SNR at Ltyp , No Saturation at Lmax
UVNIR Bands (nm) | 342.5nm – 887.5nm , 5nm Resolution
NIRSWIR Bands (nm) | 940, 1038, 1250, 1378, 1615, 2130, 2260
UVVIS & VISNIR FPAs | 2 CCDs, 128 x 512, 26 micron Integrated 14 Bit ADC
NIRSWIR FPAs | 16MCT/16InGaAs Photodiodes, < 250 micron analog output to SIDECAR ASIC
Relative Radiometric Accuracy | < 0.5% Pre-Launch 1-sigma
SNR @ Ltyp | > 1000:1: 340 – 700nm > 600:1: 700 – 865nm > 50:1 940 – 2260nm
On-Board Solar Calibration Assembly | 2 QVD Solar Calibration Targets 1 Fractal Black Solar Calibration Target
Orbital Average Data Rate | Up to 40 Mbps
Cross-Track Rotating Telescope
UVVIS & VISNIR Slit Grating Hyperspectral Spectrographs
NIR-SWIR Fiber Coupled Multiband Filter Spectrograph